## Slide 1
Computer Networking: A Top Down Approach
7th Edition, Global Edition Jim Kurose, Keith Ross Pearson April 2016
Chapter 7 Wireless and
Mobile Networks

## Slide 2: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac

## Slide 3: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
7.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet access
  architecture
  standards (e.g., 3G, LTE)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 4: Cellular Network Topology
Goal of cell : increase the available capacity for mobile service
Cell size can be determined according to the trade-off relation between deployment cost and frequency reusability
Cell을 구성하는데 많은 비용이 필요
(장비, 토지, 임대료,
관리 유지비)
도시는 조밀하게, 시골은 느슨하게

## Slide 5: Cellular Geometry
In the hexagonal pattern, distances between all pairs of antennas are equivalent
4각형, 원 구조 보다 육각형 구조가 가장 효율성이 높다

## Slide 6
Mobile
Switching
Center
Public telephone
network
Mobile
Switching
Center
Components of cellular network architecture
connects cells to wired tel. net.
manages call setup (more later!)
handles mobility (more later!)
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 7: Cellular Network 역사

## Slide 9: 1G 이동통신
아날로그 방식
음성 통신만 가능
FDMA 방식만 적용
2.4 kbps

## Slide 10
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
2G (voice) network architecture
MSC
Public
telephone
network
Gateway
MSC
G
Digital Standards
GSM = FDMA + TDMA
CDMA

## Slide 11: BTS(기지국), BSC(제어국), MSC(교환기)
기지국(BTS: Base station Transceiver Subsystem)은 이동전화와 무선 구간으로 연결되어 이동전화를 제어하고 통화채널을 연결시켜줌
제어국(BSC: Base Station Controller)은 여러 대의 기지국들을 관리하면서, 이동교환기(MSC)와 연동한다. 일부 제어국에서는 2.5세대/3세대 데이터서비스를 위하여 PDSN(라우터)과 연동 기능을 제공
교환기(MSC: Mobile Switching Center)는 이동통신망의 핵심 망요소로서, 음성통화 및 각종 부가서비스를 제어하고, 통화로를 설정하며, 여러 다른 장비들 및 외부망과의 연결기능을 제공한다.

## Slide 12: Cellular networks : GSM
Two techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots : GSM
CDMA: code division multiple access
frequency
bands
time slots

## Slide 13: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence

## Slide 14: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 15: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2

## Slide 16
3G (voice+data) network architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 17
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
G
3G versus 4G LTE network architecture
GGSN
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
MME
Public
Internet
P-GW
G
S-GW
G
HSS
3G
4G-LTE

## Slide 18
4G: differences from 3G
두 종류 : LTE(Long Term Evolution) or WiMAX
  LTE는 기존 3G망 사용, WiMAX는 백본도 무선으로
  All IP core: IP packets tunneled (through core IP network) from base station to gateway
  no separation between voice and data – all traffic carried over IP core to gateway 음성 (VoIP) 과 데이터망의 통합
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
Public
Internet
P-GW
G
S-GW
G
UE
(user element)
eNodeB
(base station)
Packet data
network
Gateway
(P-GW)
Serving
Gateway
(S-GW)
data
MME
HSS
Mobility
Management
Entity (MME)
control
Home Subscriber
Server(HSS)
(like HLR+VLR)

## Slide 19
Functional split of major LTE components
holds idle UE info
QoS enforcement
handles idle/active UE transitions
pages UE
sets up eNodeB-PGW tunnel (aka bearer)

## Slide 20
Radio+Tunneling: UE – eNodeB – PGW
tunnel
link-layer radio net
UE
eNodeB
S-GW
G
P-GW
G
IP packet from UE encapsulated in GPRS Tunneling Protocol (GTP) message at ENodeB
GTP message encapsulated in UDP, then encapsulated in IP. large IP packet addressed to SGW

## Slide 21: 5G
Requirements for 5G network (4G에 대해 성능 향상)
  Area traffic capacity (1000배)
  Peak data rate (10 Gbps) (100배)
  User experienced data rate (100 Mbps)
  5% user spectral efficiency
  Transmission latency ( < 1ms)
  Energy efficiency
  Mobility (up to 500 km/h)
  Handover interruption time ( < 10ms)

## Slide 22: 5G 응용분야
자율 주행 자동차
군사용

## Slide 23: 5G 동영상
주파수 개념
https://www.youtube.com/watch?v=L0uO6t_lowM
https://www.youtube.com/watch?v=tiA-fgRCMGw
https://www.youtube.com/watch?v=0d_4LKWDIAg&t=1054s
6G
https://www.youtube.com/watch?v=YtyhfrUpdLM

## Slide 24: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
7.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
  architecture
  standards (e.g., 3G, LTE)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 25: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 26: Mobility: vocabulary
wide area network
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote

## Slide 27: Mobility: more vocabulary
wide area network
care-of-address: address in visited network.
(e.g., 79,129.13.2)
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 28: How do you contact a mobile friend:
search all phone books?
call her parents?
expect her to let you know where he/she is?
Facebook!
I wonder where Alice moved to?
Consider friend frequently changing addresses, how do you find her?

## Slide 29: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
라우터가 직접 이동된 디바이스의 주소를 직접 관리한다면 문제가 심각
현실적으로 라우터는 서브넷 단위로 관리
포워드 테이블의 한계
  확장성 문제 (scalability)

## Slide 30: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
(호스트가 Agent 도움을 받아 해결함)
  indirect routing: (간접 라우팅)
  direct routing: (직접 라우팅)
not
scalable
to millions of
mobiles

## Slide 31: Mobility: approaches
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  간접 라우팅 방식
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 32: Mobile IP
RFC 3344
간접 라우팅 방식
has many features we’ve seen:
  home agents, foreign agents, foreign-agent registration, care-of-addresses, encapsulation (packet-within-a-packet)
three components to standard: (3 단계)
  1) agent discovery (HA 와 FA를 서로 확인함)
  2) registration with home agent
  3) indirect routing of datagrams

## Slide 33: Mobile IP : 1) Agent Discovery
Agent advertisement : foreign/home agents advertise service by broadcasting ICMP messages
(typefield = 9)
Care-of-address (COA)
Foreign agent가 외부
디바이스에게
할당하고자 하는 여분의
IP 주소

## Slide 34: Mobile IP: agent discovery
agent advertisement: foreign/home agents advertise service by broadcasting ICMP messages (typefield = 9)
R bit: registration required
H,F bits: home and/or foreign agent

## Slide 35: Agent Discovery
wide area network
care-of-address: address in visited network.
(e.g., 79,129.13.2)
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 36: Mobility: registration
wide area network
end result:
foreign agent knows about mobile device
home agent knows location of mobile
이동 장치는 새로운 COA를 하나 할당됨
HA는 이동 장치의 위치를 알게 됨
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 37: Mobile IP: registration example
visited network: 79.129.13/24
home agent
HA: 128.119.40.7
foreign agent
COA: 79.129.13.2
mobile agent
MA: 128.119.40.186
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999
identification:714
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714
encapsulation format
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714
….
time
ICMP agent adv.
COA: 79.129.13.2
….
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999
identification: 714
encapsulation format
….

## Slide 38: Mobility via indirect routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 39: Mobile IP: indirect routing
Permanent address: 128.119.40.186
Care-of address: 79.129.13.2
dest: 128.119.40.186
packet sent by correspondent
dest: 79.129.13.2
dest: 128.119.40.186
packet sent by home agent to foreign agent: a packet within a packet
dest: 128.119.40.186
foreign-agent-to-mobile packet

## Slide 40: Co-located COA
모바일 디바이스에게 직접 새로운 IP 주소를 할당할 수 있다.

## Slide 41: Indirect Routing: comments
mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
비효율적일 수 있다.

## Slide 42: Indirect routing: moving between networks
suppose mobile user moves to another network
  registers with new foreign agent
  new foreign agent registers with home agent
  home agent update care-of-address for mobile
  packets continue to be forwarded to mobile (but with new care-of-address)
mobility, changing foreign networks transparent: on going connections can be maintained!

## Slide 43: Mobility via direct routing: comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?
송신자가 수신자의 변동된 IP (COA)을 H.A을 통해 알아서 직접 FA를 거쳐서 수신자를 찿아감
1
2
3
4

## Slide 44: Mobility via direct routing
1
2
3
4
home
network
visited
network
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 45: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
7.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
  architecture
  standards (e.g., 3G, LTE)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 46
Components of cellular network architecture
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers
recall:

## Slide 47
Mobile
Switching
Center
VLR
old BSS
new BSS
old
routing
new
routing
GSM: handoff with common MSC
handoff goal: route call via new base station (without interruption)
수신되는 BSS가 바뀜 : 에너지 절약, 로더 밸린싱
reasons for handoff (handover):
  stronger signal to/from new BSS (continuing connectivity, less battery drain)
  load balance: free up channel in current BSS
handoff initiated by old BSS

## Slide 48
Mobile
Switching
Center
VLR
old BSS
1
3
2
4
5
6
7
8
new BSS
old BSS informs MSC of impending handoff, provides list of 1+ new BSSs
시그널 강도가 약함을 먼저 감지
2. MSC sets up path (allocates resources) to new BSS
3. new BSS allocates radio channel for use by mobile
4. new BSS signals MSC, old BSS: ready
5. old BSS tells mobile: perform handoff to new BSS
6. mobile, new BSS signal to activate new channel
7. mobile signals via new BSS to MSC: handoff complete. MSC reroutes call
8 MSC-old-BSS resources released
GSM: handoff with common MSC

## Slide 50
Handling Mobility in LTE
Paging: idle UE may move from cell to cell: network does not know where the idle UE is resident
  paging message from MME broadcast by all eNodeB to locate UE
handoff: similar to 3G:
  preparation phase
  execution phase
  completion phase
P-GW
old
eNodeB
old
routing
new
routing
new
eNodeB
source
MME
target
MME

## Slide 51: Mobility: cellular versus Mobile IP
cellular element |  | Comment on cellular element | Mobile IP element | 
Home system | Network to which mobile user’s permanent phone number belongs |  |  | Home network
Gateway Mobile Switching Center, or “home MSC”. Home Location Register (HLR) | Home MSC: point of contact to obtain routable address of mobile user. HLR: database in home system containing permanent phone number, profile information, current location of mobile user, subscription information |  |  | Home agent
Visited System | Network other than home system where mobile user is currently residing |  |  | Visited network
Visited Mobile services Switching Center. Visitor Location Record (VLR) | Visited MSC: responsible for setting up calls to/from mobile nodes in cells associated with MSC. VLR: temporary database entry in visited system, containing subscription information for each visiting mobile user |  |  | Foreign agent
Mobile Station Roaming Number (MSRN), or “roaming number” | Routable address for telephone call segment between home MSC and visited MSC, visible to neither the mobile nor the correspondent. |  |  | Care-of-address

## Slide 52: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handoff
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  limited bandwidth of wireless links

## Slide 53: Chapter 7 summary
Wireless
wireless links:
  capacity, distance
  channel impairments
  CDMA
IEEE 802.11 (“Wi-Fi”)
  CSMA/CA reflects wireless channel characteristics
cellular access
  architecture
  standards (e.g., 3G, 4G LTE)
Mobility
principles: addressing, routing to mobile users
  home, visited networks
  direct, indirect routing
  care-of-addresses
case studies
  mobile IP
  mobility in GSM, LTE
impact on higher-layer protocols