## Slide 1
Computer Networking: A Top Down Approach
7th Edition, Global Edition Jim Kurose, Keith Ross Pearson April 2016
Chapter 7 Wireless and
Mobile Networks

## Slide 2: Ch. 6: Wireless and Mobile Networks
Background:
현재 모바일 폰과 무선 인터넷에 연결된 장치의 수가 기존 유선 방식을 능가하고 있음
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers (5-to-1)!
# wireless Internet-connected devices =
# wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
6.73 IEEE 802.11 wireless LANs (“Wi-Fi”)
67.4 Cellular Internet Access
  architecture
  standards (e.g., 3G, LTE)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 4: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
network
infrastructure

## Slide 5: Elements of a wireless network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
network
infrastructure

## Slide 6: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 7: Elements of a wireless 기반구조
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network (handover)
Wi-Fi, cellular, WiMax (Wibro), etc
network
infrastructure

## Slide 8: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves
Multi-hop comm.
Wi-Fi Direct, Bluetooth, etc

## Slide 9: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET 이동 애드 혹 넷
VANET: 차량 에드 혹 넷

## Slide 10: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
7.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
  architecture
  standards (e.g., 3G, LTE)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 11: Wireless Link Characteristics (1)
important differences from wired link ….
  decreased signal strength: 시그널 강도가 물체 또는 거리에 따라 약해짐 (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  표준 무선 주파수 대역은 많은 기기가 공유로 무선 신호 간섭이 심함
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
  무선신호가 건물, 산, 장애물로 신호의 도착 시간이 다름
  (지연, 방해)
…. make communication across (even a point to point) wireless link much more “difficult”
비트 오류가 심함  강력한 CRC 오류 검출, 프레임 재 전송이 필요

## Slide 12: Wireless 특징 :신호대비 잡음 비율 (SNR)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR vs. BER tradeoffs [반비례]
  Given physical layer: increase power -> increase SNR->decrease BER
  Given SNR: choose physical layer that meets BER requirement, giving highest thruput
  SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps) : 좋은 환경
QAM16 (4 Mbps)
BPSK (1 Mbps) : 소음이 큰 환경
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 13: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
7.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet Access
  architecture
  standards (e.g., 3G, LTE)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 14: 무선통신의 대역폭 :wifi, wpan, celluar
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac

## Slide 15: IEEE 802.11 Wireless LAN
802.11b (1999)
2.4 GHz unlicensed spectrum
up to 11 Mbps
802.11a (1999)
  5 GHz range
  up to 54 Mbps
802.11g (2003)
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae 2009
  2.4-5 GHz range
  up to 200 Mbps (SU-MIMO)
802.11ac (14,16)
  5GHz range
  up to 866.7 Mbps(SU-MIMO), 1.73Gbps)MU-MIMO)
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions
SU-MIMO : 안테나당 하나의 유저 할당
MU-MIMO : 안테나를 여러 유저가 공유

## Slide 16: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP) 공유기
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router

## Slide 17: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
  총 80Mhz, 1채널당 20Mhz
  11개 채널이 주파수 대역을 공유 (1,6,11 주로 사용)

## Slide 18: 802.11: Channels, association
host: must associate with an AP
  AP가 먼저 자신의 존재를 알림
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet
  Beacon : 안전운행을 위한 불빛, 위치 확인을 위한 무선 송신소

## Slide 19: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 20
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for RDT)
frame type
(RTS, CTS, ACK, data)
802.11 frame: more

## Slide 21
Internet
router
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing

## Slide 22
802.11: advanced capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
802.11g supports various data rates : 6, 9,12,18,24,36,48 & 54 Mbps
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 23: CSMA, CSMA/CD in Wireless
신호를 전송하기 전에 다른 사용 여부를 감지함
충돌이 일어나면 재 전송
문제점
  만약 송신자가 시그널을 감지 못한다면?
  만약 송신자가 충돌을 감지하지 못한다면?

## Slide 24: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 25: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 26: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
DIFS > SIFS (Ack 메시지를 방해 하지 않음)
Distributed Inter-Frame Space (신호없음을 감지하는 시간)
Short Inter-Frame Space
sender
receiver
DIFS
data
SIFS
ACK

## Slide 28: Avoiding collisions (more)
Hidden Terminal Problem의 해결책
idea: allow sender to “reserve(예약)” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 29: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 30
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for RDT)
frame type
(RTS, CTS, ACK, data)
802.11 frame: more

## Slide 31
802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1
H1
BBS 2
BBS 1

## Slide 32
M
radius of
coverage
S
S
S
P
P
P
P
M
S
Master device
Slave device
Parked device (inactive)
P
802.15: personal area network
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
master/slaves:
  slaves request permission to send (to master)
  master grants requests
802.15: evolved from Bluetooth specification
  2.4-2.5 GHz radio band
  up to 721 kbps
  8개 디바이스 연결

## Slide 34: Bluetooth 4.0 : Bluetooth Smart
B. Smart : 기존 것과는 호환 불가
B. Smart Ready : 기존 것과 호환 가능
  슬래브가 항상 대기 상태가 아님
  전력 손실이 적음

## Slide 35: Bluetooth 5
신뢰성, 속도 등이 향상
거리, 데이터 양이 증가

## Slide 36: Zigbee
2001년도 MIT에서 개발
소형, 저전력 디지털 라디오 주파수를 이용하여 개인 통신망을 구축하기 위한 표준
긴 베터리 수명과 보안성이 요구되는 분야에서

## Slide 37: Zigbee 활용도
스마트 에너지분야
홈 엔터테인먼트와 제어 (온도 조절, 영화/음악)
홈 인식 시스템 (수온센서, 화재 및 도난 센서)
모바일 서비스 (모바일 결제, 모니터링, 헬스케어)
상업빌딩 (에너지 감시, 공기정화시설, 조명,출입)
산업용 공장 (자재관리, 환경관리, 에너지 관리)

## Slide 39: Chapter 7 outline
7.1 Introduction
Wireless
7.2 Wireless links, characteristics
  CDMA
7.3 IEEE 802.11 wireless LANs (“Wi-Fi”)
7.4 Cellular Internet access
  architecture
  standards (e.g., 3G, LTE)
Mobility
7.5 Principles: addressing and routing to mobile users
7.6 Mobile IP
7.7 Handling mobility in cellular networks
7.8 Mobility and higher-layer protocols

## Slide 40: Background
Wireless (무선) 네트워크
  무선을 통해서 통신이 가능
모바일
  사용자가 접속하는 네트워크의 범위를 바꿀 수 있도록 지원

## Slide 41: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
Point (Bluetooth)
mobile user, passing through multiple access point while maintaining ongoing connections
(like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.
Wifi

## Slide 42: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence

## Slide 43: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 44: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2